## Slide 1: Automated Reasoning about Software ()
Guy Katz
Lecture : SAT Solver Applications and Challenges November th,

## Slide 2: Acknowledgements
Some of the material presented has been borrowed from slides by David Dill, Isil Dillig, Gera Weiss, Clark Barrett, Alex Aiken, Moshe Vardi, Mooly Sagiv and Ofer Strichman

## Slide 3: Overview
Previously: architecture of modern solvers
  DPLL ,CDCL
Today: some SAT solver applications
  Product configuration
  Hardware manufacturing
  Bounded model checking
Some variations and challenges

## Slide 4: Some History
s:
  Futile efforts to show that search problems are hard
Stephen Cook, :
  SAT is NP-complete
Richard Karp, :
  additional NP-Complete problems, including Clique, Vertex Cover, Set Covering, Hamiltonian Cycle, Coloring, Knapsack, etc

## Slide 5: Some History (cnt’d)
In the ’s, SAT was a scary problem
  “Not to be touched with a -foot pole”
Even today, some small instances cannot be solved
However, solvers widely used in industry, routinely solve problems with millions of variables
  Almost considered an easy problem

## Slide 6: Today’s Landscape in SAT Solving
Very active field, annual conference for years
CDCL solvers can scale to problems with hundreds of thousands or even millions of variables
The annual SAT competition: www.satcompetition.org
Large problems can often be solved, but even small instances can be difficult
  Some overfitting, even in the competition
  The community is looking for more benchmarks

## Slide 7: SAT Solver Speedups

## Slide 8: P and NP
:
  Conceivably, NP-complete problems can be solved in polynomial time, but the polynomial is – impractical
  Conceivably, NP-complete problems can be solved in – practical
And in general, worst-case behavior not encountered in practice
Better ways for measuring a problem’s difficulty are needed

## Slide 9: Why Focus on SAT?
Many interesting problems can be reduced to SAT
Idea: write highly optimized SAT solver, and use it to solve any NP-complete problem
  However, the encoding matters a lot
    Often the case in many verification tools
  Knowing something about CDCL is useful

## Slide 10: Validity
A propositional formula is valid if it evaluates to for any assignment
How can we check this using a SAT solver?
  Check the satisfiability of
Is the validity problem NP-complete?
  It is co-NP complete

## Slide 11: A Small Yet Difficult Problem
The pigeonhole problem
Is it possible to place pigeons into holes?
Obvious for humans
But, turns out to be quite difficult for SAT solvers

## Slide 12: The Pigeonhole Problem
Encode this for (UNSAT)
: pigeon placed in ’th hole
’th pigeon must be placed in at least one hole:
Every pigeon must be placed in precisely one hole:

## Slide 13: The Pigeonhole Problem (cnt’d)
In addition: multiple pigeons can’t share a hole
With , competitive solvers cannot solve
Problem: conflicts include specific pigeons/holes, not generalized through symmetry
Symmetry breaking is an active research

## Slide 14: Application: Product Configuration
Motivation: some products are highly customizable
Example: Mercedes C class – options
  Leather interior, built-in GPS, seat heating, thermotronic comfort air conditioning, high-capacity battery, ventilate seats, etc.
  But there may be dependencies!
  Example: “Thermotronic comfort air conditioning requires high-capacity battery except when combined with gasoline engines of liter capacity”
  Need to prevent inconsistent configurations

## Slide 15: Configurations using SAT
Idea: use a SAT solver to check for consistency
Encode dependencies as propositional formula
Encode user selection as another formula
Use solver to check whether is SAT
  If yes, then configuration is fine

## Slide 16: Example: Configurations using SAT
Dependency: Thermotronic comfort air conditioning requires high-capacity battery except when combined with gasoline engines of liter capacity
  : thermotronic comfort air conditioning
  : high-capacity battery
  : gasoline engine with liter capacity
Consistency requirement:
If user selects , the solver will warn us

## Slide 17: Application: ATPG
SAT solvers can be used in testing integrated circuits
A common problem in circuits: a component is stuck at fault
  Output stuck on or , regardless of input
Automatic test pattern generation (ATPG) is used in constructing inputs that check this

## Slide 18: ATPG Using SAT
Encode the circuit as two propositional formulas
  First: “the good circuit” – the circuit without any faulty components
  Second: “the faulty circuit” – represents the circuit with a particular component stuck at fault
Use solvers to find inputs that produce different outputs on the two circuits

## Slide 19: Example: ATPG Using SAT
Good circuit:
Faulty circuit:
The “or” component is stuck at

## Slide 20: Example: ATPG Using SAT (cnt’d)
Good circuit output :
Faulty circuit output :
Solve:
Satisfying assignment is a good test case!

## Slide 21: Model Checking
An automated method for verification
Given a system model and a property , check that satisfies or provide a counterexample
Examples for properties:
  Can the system reach a deadlock?
  Can two threads simultaneously enter a critical section?
  Does the system produce the correct output?
Different kinds of models and properties

## Slide 22: Model Checking (cnt’d)
All possible executions
Executions satisfying property
Program executions
Counterexample

## Slide 23: Model Checking: Advantages
Widely applicable (software, hardware, protocols, etc.)
Allows partial verification – only the most relevant properties
Fully automated, and provides mathematical guarantees
Complete coverage, not just common scenarios
Provides a counterexample when property fails

## Slide 24: Model Checking: Disadvantages
Usually checks the control flow of reactive systems, not so much the accuracy of computations
Model quality plays a crucial role
Key problem: state explosion

## Slide 25: Model Checking: Safety Properties
Simple case:
  Model is a transition system
  Safety property: bad things do not happen
    Some states in the transition system marked as bad
Verification: are any bad states reachable from the initial state?
Linear in the size of the transition system
  State explosion: models can be huge (exponential in program size)
  Can even be infinite

## Slide 26: Example: Mutual Exclusion
Goal: check that never
While True do
Wait (Turn = 0)
Turn
While True do
Wait (Turn = )
Turn

## Slide 27: Example: Mutual Exclusion (cnt’d)
Model this program as a transition system
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn

## Slide 28: Scaling-Up Model Checking
Symbolic model checking
  Represent many system states as one symbolic state in the transition graph
  Often means the use of Binary Decision Diagrams (BDDs)
Compositional verification
  Verify components separately, deduce global correctness
Reductions, such as Partial Order Reduction
Bounded model checking

## Slide 29: Bounded Model Checking
Idea: only explore a part of the transition system
  Usually, up to steps from initial state
Still guarantees absence of bugs, but only up to steps
Weaker than model checking, but much more scalable
  A very widespread technique!
Utilizes SAT solvers

## Slide 30: Bounded Model Checking (cnt’d)
The variables represent system states
Initial states: a predicate , true iff is initial
Transition relation: iff is reachable from in one step
Safety property: , true iff property holds at state

## Slide 31: Bounded Model Checking (cnt’d)
The BMC query:
Note: is negated, to look for errors
is UNSAT iff property holds for any execution of length at most

## Slide 32: Example: Two Bit Counter
State variables:
Initial state:
Transition:
Property: always
UNSAT for , SAT for

## Slide 33: Safety and Liveness
Safety: bad things never happen
  Check whether there are reachable bad states
Liveness: good things eventually happen
  Check whether there are reachable cycles without good states

## Slide 34: Example: Shift Left
State machine with bits:
Initial state: unknown
Transition relation:
Property: register is eventually
  “Good things eventually happen” – a liveness property

## Slide 35: Example: Shift Left (cnt’d)
Look for violations of length up to
A violating execution must include a loop:
And this loop must not include the state 000
Verification query:

## Slide 36: Example: Shift Left (cnt’d)
SAT solver returns counter example: all variables are

## Slide 37: BMC With Increasing Lengths
If UNSAT, can iteratively increase
BMC(
++
Yes
No

## Slide 38: How Large Should k Be?
For finite transition systems, there is always a such that
For particular classes of properties, lower thresholds exist
Can settle for approximations

## Slide 39: -Induction
BMC is aimed at finding violating runs
  Refuting properties
-Induction is a related approach for proving properties
Suppose we wish to prove the property: always
  A safety property
If we can prove that:
  holds initially
  If state satisfies , the successors of satisfy
Then by induction, always holds

## Slide 40: -Induction (cnt’d)
Unfortunately, this approach rarely works
  Even when the property does hold
Why?
  Unreachable states!

## Slide 41: -Induction (cnt’d)
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn

## Slide 42: A Better Method
Check that states reachable from the initial state in steps satisfy
  Using BMC
Check that if holds on all -long paths, then it also holds for state number
  Doesn’t have to start from the initial state
  Can also be encoded into SAT
Together, this proves the desired property

## Slide 43: -Induction (cnt’d)
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn
Turn

## Slide 44: Further Improvements?
Consider the following situation:
For which can we prove correctness using induction?
We can change the encoding to consider only loop-free paths

## Slide 45: Other Variations of SAT
The basic satisfiability problem: given a propositional formula , is satisfiable?
Common variations:
  Maximum Satisfiability (MaxSAT)
  Partial MaxSAT
  Weighted MaxSAT
  UNSAT Cores

## Slide 46: Maximum Satisfiability (MaxSAT)
MaxSAT: Given a formula in CNF, find an assignment that maximizes the number of satisfied clauses in
  Observe: if is SAT, the answer is just a satisfying assignment (all clauses will be satisfied)
If is UNSAT, we want to find a maximal subset of clauses whose conjunction is SAT
Example:
Maximal number of satisfied clauses:

## Slide 47: Partial MaxSAT
Similar to MaxSAT, but we distinguish between clauses:
  Hard clauses: must be satisfied
  Soft clauses: should, but don’t have to be, satisfied
Partial MaxSAT: given a CNF formula , where each clause is marked soft or hard, find an assignment that satisfies all the hard clauses and maximizes the number of satisfied soft clauses

## Slide 48: Partial MaxSAT (cnt’d)
Regular SAT and MaxSAT are special cases of partial maxSAT
  Regular SAT: all clauses are hard
  MaxSAT: all clauses are soft
Partial MaxSAT is a generalization of SAT and MaxSAT

## Slide 49: Partial Weighted MaxSAT
Yet another generalization
Soft clauses also have weights
  A way to indicate importance
The goal: find an assignment that maximizes the weights of satisfied soft clauses
Partial MaxSAT is a private case, where all clauses have equal weights

## Slide 50: Partial MaxSAT Application
Software package installation: you want to install software package , but it has dependencies
  Example: requires , and is not compatible with package
  requires and is not compatible with
Some packages (e.g., ) may already be installed
Question:
  Can you install ?
  Which software should you uninstall to install ?

## Slide 51: Partial MaxSAT Application (cnt’d)
Can phrase this as a MaxSAT instance
  Goal: install :
  requires :
  incompatible with :
  requires :
  incompatible with :
  already installed:
SAT: can install , and assignment will indicate dependencies that need to be installed
Partially SAT: violated soft clauses will indicate what to uninstall
Hard
Soft

## Slide 52: Summary
Modern SAT solvers can handle hundreds of thousands of variables
  Huge improvement in last years
  Many mature tools available
  Active research, annual conferences and competition
Some applications:
  Product configurations
  Automatic test pattern generation
  Bounded model checking (safety and liveness properties)
Other variants: MaxSAT, (Weighted) Partial MaxSAT